## Slide 1: Welcome! Overview of ISO Location Codes
Version: 5 April 2026
This file is set to be viewed in presentation mode.

## Slide 2: ISO Location Codes
Notes: Códigos de ubicación ISO
Ejemplo : LT5N =
L = lado izquierdo ( left )
T = parte de arriba ( top )
5N = panel numero 5

## Slide 3: ISO/CEDEX 9897 Container Equipment Data Exchange
1st Character identifies the face of the container. | 
Right Side | R
Left Side | L
Roof / Top | T
Bottom / Floor | B
Front End (opposite of Door side) | F
Door End | D
Understructure | U
Whole Container | X
Container Interior | I
Container Exterior | E
A combination of 4 alpha & numeric codes.

## Slide 4: ISO/CEDEX 9897 Container Equipment Data Exchange
2nd Character identifies the horizontal seperation |  | 
High – Upper Component | H | 
Top – Top Half | T | 
Bottom – Bottom Half | B | 
Ground – Lower Component | G | 
Both Halves; or all 4 horizontal zones | X (H, T, B, G) | 
Neutral, no further character needed | N (can only be used as 4th character code) | 
Specific for ROOF ¦ BOTTOM ¦ UNDERSTRUCTURE |  | 
Right Half | R | No separation in right or left half for the INTERNAL or EXTERNAL section. This is either IXXX or EXXX.
Left Half | L | 
Both Halves | X | 
A combination of 4 alpha & numeric codes.
“X” if damage covers the entire length of the container face, use “X” as the 3rd and 4th character codes

## Slide 5: ISO/CEDEX 9897 Container Equipment Data Exchange
3rd + 4th Character identifies the vertical separation | 
20ft containers | 5 sections long
40ft containers | 10 sections long (e.g. RB48, LT80
Section 10 is represented via the figure 0  1 ¦ 2 ¦ 3 ¦ 4 ¦ 5 ¦ 6 ¦ 7 ¦ 8 ¦ 9 ¦ 0 | 
Damage across the full length | X  instead RB10, it would be RBXX
A combination of 4 alpha & numeric codes.

## Slide 6: ISO/CEDEX 9897 Container Equipment Data Exchange
Horizontal Position – Count always starts at the door end side.
Right Side
X

## Slide 7
H
G
T
B
DOOR
Left Side
FRONT
X

## Slide 8: ISO/CEDEX 9897 Container Equipment Data Exchange
Vertical position.
H > HIGH
T > TOP
B > BOTTOM
G > GROUND

## Slide 9
H
G
T
B
Doors
1
4
2
3
X

## Slide 10
H
G
T
B
Front
Follows the door positions
4
1
2
3
X

## Slide 11: Floor Face = B (first character) Underside = U (first character)

## Slide 12
Right Side
RT2N
RB23
RX0N
RG6N

## Slide 13
H
G
T
B
Doors
DH2N
DB1N
1
4
2
3
X

## Slide 14
H
G
T
B
Front
FB3N
4
1
2
3
Follows the door positions
X

## Slide 15: TL3N
TX9N
Roof = T
Doors

## Slide 16
BL1N
IXXX

## Slide 17
BR80
BL0N

## Slide 18
Left Side
UX8N
UL9N
Right Side
UR8N

## Slide 19: Thanks for watching it. We hope this presentation was useful to you.
If you have questions or suggestions, please contact: technical@iicl.org
Setting Industry Standards for 55 Years.